Structure of Recorded File in TF5000PVR

| Date Issued | Revision | Author | Description of Change |
| --- | --- | --- | --- |
| 2004.2.21 | v1.0 | MJ Kim | - |

☞ Table of Contents ☜

1.	Basic Structure	3

2.	SERVICE_INFO	3

3.	TP_INFO	4

4.	EVT_INFO	4

5.	EXT_EVT_INFO	5

6.	TS_DATA	5

# Basic Structure

TF5000PVR_RECORDED_SERVICE_HEADER ( )

{

| FIELD NAME | No. of bits | Identifier | Remarks |
| --- | --- | --- | --- |
| Id | 8 * 4 | Bslbf | “TFrc” |
| Version | 16 | Uimsbf | 0x5000 |
| RESERVED | 16 | Bslbf | Reserved for future use |
| Duration | 16 | Uimsbf | Minutes |
| Service_Number | 16 | Uimsbf | Service number in channel list. It does not matter for playback. |
| Service_Type | 16 | Bslbf | 0 : TV 1 : Radio |
| SERVICE_INFO |  |  | STRUCTURE |
| TP_INFO |  |  | STRUCTURE |
| EVT_INFO |  |  | STRUCTURE |
| EXT_EVT_INFO |  |  | STRUCTURE |
| TS_DATA |  |  | Transport Stream data |

}

- The fields of Id and Version shall be matched with the firmware which is released after Feb. 23 2004.

# SERVICE_INFO

SERVICE_INFO ( )

{

| FIELD NAME | No. of bits | Identifier | Remarks |
| --- | --- | --- | --- |
| RESERVED | 26 | Bslbf | Reserved for future use |
| Tuner_Info | 6 | Bslbf | Tuner information when recording is started. It does not matter for playback. 100000b : Tuner 1 010000b : Tuner 0 |
| Service_Id | 16 | Bslbf | Service ID of TS stream |
| PMT_PID | 16 | Uimsbf | PID number of PMT TS packet |
| PCR_PID | 16 | Uimsbf | PID number of PCR TS packet |
| VIDEO_PID | 16 | Uimsbf | PID number of Video TS packet |
| AUDIO_PID | 16 | Uimsbf | PID number of Audio TS packet |
| Service_Name | 8 * 24 | Bslbf | File Name |

}

# TP_INFO

TP_INFO ( )

{

| FIELD NAME | No. of bits | Identifier | Remarks |
| --- | --- | --- | --- |
| Satellite_Index | 8 | Uimsbf | Satellite index of recorded channel |
| Polarity | 1 | Bslbf | It does not matter for playback. |
| RESERVED | 23 | Bslbf | Reserved for future use |
| Frequency | 32 | Uimsbf | It does not matter for playback. |
| Symbol_Rate | 16 | Uimsbf | It does not matter for playback. |
| Transport_Stream_Id | 16 | Uimsbf | It does not matter for playback. |
| RESERVED | 32 | Bslbf | Reserved for future use |

}

# EVT_INFO

EVT_INFO ( )

{

| FIELD NAME | No. of bits | Identifier | Remarks |
| --- | --- | --- | --- |
| RESERVED | 16 | Bslbf | Reserved for future use |
| Duration | 16 | Uimsbf | Minutes |
| Event_Id | 32 | Uimsbf | Event ID |
| Start_Time_MJD | 16 | Uimsbf | MJD (Modified Julian Date) of start time |
| Start_Time_Hour | 8 | Uimsbf | Hour of start time. |
| Start_Time_Min | 8 | Uimsbf | Minute of start time |
| End_Time_MJD | 16 | Uimsbf | MJD (Modified Julian Date) of end time |
| End_Time_Hour | 8 | Uimsbf | Hour of end time. |
| End_Time_Min | 8 | Uimsbf | Minute of end time |
| RESERVED | 8 | Bslbf | Reserved for future use |
| Event_Name_Length | 8 | Uimsbf | Length of event name in Event text |
| Parental_Rate | 8 | Uimsbf | Parental rate |
| Text | 8 * 129 | Bslbf | Event text (Name + Short Descriptor) |
| RESERVED | 8 * 12 | Bslbf | Reserved for future use |

}

# EXT_EVT_INFO

EXT_EVT_INFO ( )

{

| FIELD NAME | No. of bits | Identifier | Remarks |
| --- | --- | --- | --- |
| RESERVED | 8 * 6 | Bslbf | Reserved for future use |
| Text_Length | 16 | Uimsbf | Length of Extended Event Text |
| Event_Id | 32 | Uimsbf | Event ID |
| Text | 8 * 1024 | Bslbf | Extended Event Text |
| RESERVED | 8 * 52 | Bslbf | Reserved for future use |

}

# TS_DATA

- TS data should be completely aligned in 188 TS packet unit.